## Slide 1
Venkat Rangan
tinyNX33U Module v1:
Early Access Documentation

## Slide 2: What is it?
25.4mm x 25.4mm x 4.5mm module, Commercial temperature
  2x Hirose high density DF40C 60 pin connectors
    Proven on 1000’s of SoM’s in the field in high vibration environments
    Spare pins for future proofing
2 flavors:
  Connectivity: 14 diff pairs, no SSRAM
  Compute: 8 diff pairs, 32 MB oSPI/HyperRAM @ <0.5GBps
Interfaces
  3x fully programmable clocks
  GPIO, I2C, field updates through FPGA or direct flash programming
  GPIO voltage is programmable
Firmware/RTL
  uPython for control path on RISCv
  No code, graphical RTL generator with large # of IP blocks (under development)
Development Boards
  Baseboard for programming/debug
  Camera and other expansion boards available
NX33U
SRAM
Flash
Clock
Power

## Slide 3: SoM Interface
2x Hirose DF40C 60 pin connectors
  Low cost, high performance, easily available
3mm mounting hole for mechanical stability

## Slide 4: Baseboard
Debug USB
SoM Enable
FTDI Disable
INITn
USBC I2C Enable
USBC
LED: 5V
LED: 3.3V
GPIO_DIR/CLK_EN
LED: DONE